## Slide 1
PaddyGuard
Deep Learning-Based Rice Leaf Disease Detection & Variable-Rate Chemical Spraying System
Review III — Panel Review
Based on Tewari et al. (2020) methodology

## Slide 2
Problem Statement & Objective
Problem
• 20-40% of global crop yield lost to plant diseases
• Traditional uniform spraying wastes chemicals & harms environment
• Manual disease diagnosis is slow and subjective
• Existing systems lack real severity measurement
Our Solution
• CNN classifier identifies the disease type (6 classes incl. Healthy)
• Trained segmentation model measures actual diseased area
• Disease-specific dosing: different diseases get different spray intensity
• Variable-rate spray: solenoid open time proportional to severity
• Interactive web demo for real-time diagnosis

## Slide 3
System Architecture — Pipeline
1. Upload
User uploads a leaf image
2. Classify
EfficientNetV2-B0 identifies disease
3. Segment
U-Net detects lesion pixels
4. Severity
diseased ÷ leaf = severity %
5. Spray
C_eff → solenoid open time (t_s)
Key novelty: The CNN diagnoses WHICH disease; segmentation measures HOW MUCH. These are independent — the disease type then scales the spray dose via a per-disease factor. Interactive leaf tracing (MobileSAM / free-form polygon) isolates the main leaf from cluttered backgrounds.

## Slide 4
Modules Implemented
Module | Method | Status
Disease Classifier | EfficientNetV2-B0 (transfer learning) | Trained & deployed
Lesion Segmenter | U-Net (MobileNetV2 encoder), Dice+BCE | Trained & deployed
Leaf Isolation | MobileSAM + free-form lasso | Deployed
Severity Measurement | diseased px ÷ leaf px × 100 | Deployed
Disease-Specific Dosing | Per-disease factor × base coefficient | Deployed
Variable-Rate Spray | Standardized solenoid timing (0.5–3.0s) | Deployed
Confidence Gate | Flag uncertain predictions (<70%) | Deployed
Web Demo (PaddyGuard) | Flask + animated frontend (3 tabs) | Deployed

## Slide 5
Classifier Results — 3-Class Model (UCI Dataset)
Held-out test set: 164 images the model never saw
Class | Precision | Recall | F1 | Support
Bacterial leaf blight | 1.00 | 1.00 | 1.00 | 55
Brown spot | 0.86 | 0.89 | 0.87 | 54
Leaf smut | 0.89 | 0.85 | 0.87 | 55
Overall accuracy |  |  | 0.915 | 164
Bacterial leaf blight classified perfectly. The small error is Brown spot ↔ Leaf smut (visually similar tan lesions). 91.5% on a fully held-out set shows the architecture works well when class data is sufficient.

## Slide 6
Classifier Results — 6-Class Merged Model
Held-out validation: 815 images · 4 of 6 classes evaluated (HF dataset)
Class | Precision | Recall | F1 | Support
Neck_Blast | 1.00 | 1.00 | 1.00 | 206
Healthy | 0.83 | 0.88 | 0.85 | 288
Brown_Spot | 0.73 | 0.74 | 0.73 | 126
Blast | 0.74 | 0.67 | 0.71 | 195
Overall accuracy |  |  | 0.838 | 815
Neck blast: perfect (1.00) · Healthy: strong (0.85) — the spray/ don't-spray decision is reliable. Blast vs Brown spot are the weaker pair (both tan lesions). Bacterial Blight & Leaf Smut (55 imgs each) — known data limitation.

## Slide 7
Lesion Segmenter Results
Evaluated on PlantSeg validation set: 1,247 images with expert pixel masks
Metric | Our U-Net | PlantSeg Best (SegNext) | PlantSeg DeepLabV3+
Mean IoU | 0.4450 | 0.4452 | 0.2508–0.2718
Mean Dice | 0.5641 | — | —
Our lightweight binary U-Net (MobileNetV2 encoder) achieves 0.445 IoU — on par with the PlantSeg paper's BEST baseline (SegNext-MSCAN-L at 0.4452 mIoU) while being far smaller and faster. Note: PlantSeg baselines are on 115-class multi-disease segmentation; our task is simpler (binary lesion vs not), but the comparison demonstrates competitive pixel-level disease detection on in-the-wild images. The trained model clearly outperforms the classical colour-threshold method on cluttered field photos.

## Slide 8
Severity → Variable-Rate Spray Mapping
Severity % | Level | Base C | Bact. blight (×1.2) | Brown spot (×1.0) | Leaf smut (×0.8) | Spray time
0 (Healthy) | Healthy | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 s
0.1 – 5 | Low | 0.30 | 0.36 | 0.30 | 0.24 | ~1.1–1.4 s
5.1 – 20 | Medium | 0.55 | 0.66 | 0.55 | 0.44 | ~1.6–2.2 s
> 20 | High | 0.80 | 0.96 | 0.80 | 0.64 | ~2.1–2.9 s
Equations (Tewari et al. 2020): a = (C_eff × A) / (d × 10) [mL/hill] A=500 L/ha, d=25 hills/m² t_s = t_min + C_eff × (t_max − t_min) t_min=0.5s, t_max=3.0s Solenoid timing standardized to a real 0.5–3.0s valve window (UNL Extension G2302; Agriculture 2024, 14(3), 361). Disease-specific factors ensure the CNN's diagnosis genuinely affects the spray dose.

## Slide 9
Robustness & Safety Features
Confidence Gate (70%)
Sub-70% predictions flagged as 'uncertain' — stops the system from asserting shaky guesses.
Severity Floor (1.5%)
If diseased area < 1.5% of leaf, treated as Healthy → no spray. Eliminates false positives from stray specks.
Graceful Fallbacks
Trained segmenter → colour method; SAM → auto leaf mask. Every component degrades gracefully if unavailable.
Interactive Leaf Tracing
Free-form polygon drawn by user becomes the leaf mask. Solves the 'background counted as leaf' problem.

## Slide 10
Known Limitations & Future Work
Current Limitations
• Bacterial Blight & Leaf Smut: only 55 training images each → weakest classes
• Blast vs Brown Spot confusion (visually similar tan lesions)
• Field-photo segmentation imperfect on very cluttered backgrounds
• Spray timing (0.5–3.0s) is a research-backed default, not hardware-calibrated
• PlantSeg segmenter evaluated at 0.445 IoU — strong but not pixel-perfect
Future Work
• Collect more balanced training data for weak classes (biggest accuracy lever)
• Higher input resolution (299/384 px) to distinguish similar lesions
• Larger backbone (EfficientNetV2-B2/B3) for better feature extraction
• Hardware calibration: measure actual pump/nozzle → tune spray timing
• Deploy on edge device (TFLite on Raspberry Pi / ESP32 for field use)

## Slide 11
Live Demo
python app/server.py → http://127.0.0.1:5000
1. Upload a rice leaf image (drag & drop) 2. Auto-analysis: disease class + severity + spray decision 3. Trace around the main leaf for precise isolation 4. Watch: animated severity formulas → disease-specific dosing → spray hose animation 5. History tab: browse all past analyses 6. About tab: pipeline explanation

## Slide 12
Thank You
Questions?
PaddyGuard · EfficientNetV2-B0 + U-Net Segmentation + MobileSAM Based on Tewari et al. (2020) methodology